## Slide 1
www.bennettcustomaudio.ca
bennettcustomaudio@gmail.com
Custom Dual Overdrive
Introduction:
This custom-designed pedal features two independent overdrive circuits with order switching. The overdrives are modified versions of the Marshall BluesBreaker (“BB”), and the Zendrive by Hermida Audio (“Zendrive”). This pedal must be powered by a 9-18VDC, centre-negative power supply, capable of delivering 100mA of current – It does not have room for a battery inside. Like all our pedals, This pedal was designed and assembled by hand in St. John’s, NL.
Controls:
BB VOL: Controls the output level of the BB. Turn it up for a louder signal.
BB GAIN: Determines the amount of distortion in the BB. Turn it up for a more distorted, sustaining tone with more harmonics. Turn it down for a cleaner sound.
BB CLEAN: A clean blend control that allows you to blend in some of the input signal in with the output signal of the overdrive. Counter-clockwise gives no clean signal, turning it up gives increasingly more clean signal in the output.
BB PRESENCE: Enables fine-tuning of the overall brightness of the BB. We recommend turn it all the way counter-clockwise to start, then increase to taste if you find the tone to be too warm.
BB TREBLE: Controls how warm or bright the BB output will be. Turn it down for a warmer tone, up for a brighter tone.
ZEN VOL: Controls the output level of the Zendrive. Turn it up for a louder signal.
ZEN GAIN: Determines the amount of distortion in the Zendrive. Turn it up for a more distorted, sustaining tone with more harmonics. Turn it down for a cleaner sound.
ZEN TONE: Controls how warm or bright the tone will be. Turn it up for a bright sound.
ZEN VERSION SWITCH: Sets the “version” of the Zendrive. Version I is brighter, with asymmetric clipping, less bass, and less overall gain. Version II has more gain, bass, and symmetric clipping for a warmer, fuzzier tone.
ZEN VOICE: Sets the pre-gain bass of the Zendrive. Turning it down gives a warmer, less distorted sound. Turning it up gives a brighter sound with more overall gain.
BB Footswitch: Toggles the BB on or off with true bypass. IF the LED next to it is illuminated, your signal is passing through the effect.
Order Switch: Sets the order of the two overdrive circuits. UP puts the Zendrive before the BB in your signal chain, DOWN puts the BB before the Zendrive.
ZEN Footswitch: Toggles the Zendrive on or off with true bypass. IF the LED next to it is illuminated, your signal is passing through the effect.
V1.0.0